TSK- U5950.01A		 Fire Watch Duties

A fire watch is sometimes needed when there has been a reduction in a facility’s life-safety feature or a potentially hazardous condition exists.  As an example, part of a building’s detection or alarm system may not operate normally due to a malfunction.  Fire watches are sometimes required by local and state regulation.

The express purposes for assigning a person to an area or building as a fire watch are:

- Notifying the fire department, the building occupants, or both of an emergency,

- Preventing a fire from occurring,

- Extinguishing a small fire, if possible, and

- Protecting the public from fire or changes in life-safety conditions.

When a fire watch is determined necessary, the fire watch personnel will be provided a copy of this task outline, available at EHS-Fire Safety website or www.wwu.edu/ehs.

When assigned the duties of a fire watch, the responsible person:

- Conducts an on-going, roving surveillance of the assigned area, which would include moving between floors in a multi-floor building.

- Knows the designated Building Assembly Points and the function of Building Coordinators and Floor Wardens (see Attachments A and B)

- Wears clothing or badge that identifies them at all times, such as uniform, orange vest, or ID badge with picture.

- Immediately sounds the alarm if a fire emergency occurs.  Does this in the following ways:

  - Pulls the nearest pull station, if fire alarm system is functional

OR

Calls 650-3911 (University Police Dispatch) from a safe place

  - Notifies persons in the immediate area.

- Initiates evacuation from the building.

- Uses a fire extinguisher ONLY if trained to on a small fire and able to do so without danger to self or others.

DOES NOT delay notification or evacuation to fight a fire.

- Closes doors and windows while leaving, if it can be done safely.

- Assembles occupants at the Building Assembly Point or in a safe place, upwind, while waiting for emergency responders,

- Meets the responding University Police vehicle and provides as much pertinent information as possible about the emergency.

- Waits outside at the police vehicle or near the responding fire truck to provide assistance.

How to Use a Portable Fire Extinguisher

Remember the acronym, “P.A.S.S:”

| P | Pull the pin. Some extinguishers require releasing a lock latch, pressing a puncture lever or taking another first step |
| --- | --- |
| A | Aim low. Point the extinguisher nozzle (or its horn or hose) at the base of the flames |
| S | Squeeze the trigger or handle while holding the extinguisher upright. This releases the extinguishing agent. |
| S | Sweep the extinguisher from side to side. Keep the extinguisher aimed at the base of the fire and sweep back and forth covering the area of the fire with the extinguishing agent until it appears to be out. Watch the fire area. If the fire breaks out again, repeat the process. |

Hazards and Precautions for Fighting a Fire with a Portable Extinguisher

Only attempt to fight a fire if:

- Everyone has left or is leaving the building;

- The fire department has been called;

- The fire is confined to a small area, such as a wastebasket size;

- You can keep an exit to your back; and

- Your extinguisher is the proper size and type for the fire at hand and you know how to use it.

Otherwise depart immediately, and leave the fire for the fire department.

Environmental Health and Safety 650-3064, http://www.wwu.edu/depts/ehs   ehs@wwu.edu

| Attachment A-Building/Department Assembly Points Building/Department Assembly Points |
| --- |
| Academic Instructional Center East | South Campus Oval at Communications Facility |
| Academic Instructional Center West | South Campus Oval at Communications Facility |
| Administrative Services (A) | Parking area/lawn near building |
| Archives | Walkway near building entrance |
| Ohio Street Scene Shop | Tree in parking lot along fence line |
| Arntzen Hall | Haskell Plaza |
| Bond Hall | Red Square |
| Campus Services | Parking area by main entrance |
| Canada House | Parking area by Performing Arts Center |
| Carver Gymnasium | Walkway between Red Square and Haskell Plaza |
| College Hall | Walkway in front of building |
| Commissary | Parking area near building |
| Communication Facility | South Campus Oval at Communications Facility |
| Environmental Studies | South Campus Oval at Communications Facility |
| Fairhaven Administration | 12 A Parking lot |
| Fraser Hall | Red Square |
| Haggard Hall | Red Square |
| Humanities | Red Square |
| Miller Hall | Red Square |
| Old Main | Old Main Green |
| Parks Hall | Haskell Plaza |
| Performing Arts Center | Big red sculpture between VU and PAC |
| Single Department Buildings |
| Alumni House | Alumni House lawn |
| Art Annex | Walkway between Red Square and Haskell Plaza |
| Biology | Haskell Plaza |
| Bookstore | Walkway near building entrance by Viking Union |
| Birnam Wood Apartments | To nearest parking area |
| Buchanan Towers | Tennis Court to west |
| Chemistry | Haskell Plaza |
| Edens North | 7G parking lot |
| Edens Hall | Old Main Lawn |
| Engineering Technology (Ross) | Haskell Plaza |
| Fairhaven Residence Halls | 12A Parking lot |
| Fine Arts | Walkway between Red Square and Haskell Plaza |
| Higginson Hall | 7G parking lot |
| High Street Hall | Sidewalk in front of building |
| Highland Hall | 15R parking lot north of Commons |
| Lakewood | End of Service Road adjacent to the Boathouse |
| Marshalling Yard | Gravel parking area adjacent to loading dock |
| Mathes Hall | Parking lot 6V to southwest |
| Nash Hall | Parking lot 4R to west |
| Physical Plant | Vacant lot directly across the street from the Physical Plant |
| Recycling Center | Area in front of building |
| Ridgeway Alpha | 15R Parking lot north of Commons |
| Ridgeway Beta | Ridgeway Tennis Courts |
| Ridgeway Commons | 15R Parking lot north of Commons |
| Ridgeway Delta | Ridgeway Tennis Courts |
| Ridgeway Gamma | Ridgeway Tennis Courts |
| Ridgeway Kappa | Ridgeway Tennis Courts |
| Ridgeway Omega | 15R Parking lot north of Commons |
| Ridgeway Sigma | 15R Parking lot north of Commons |
| Science Math & Technology Education | Green in front of building |
| Shannon Point | Open Area in front of main building |
| Steam Plant | Parking area near building |
| Student Recreation Facility | Walkway and plaza in front of building |
| Viking Commons | Walkway in front of building |
| Viking Addition & Union | Performing Arts Center Plaza or Garden Street |
| Wilson Library | Red Square |

Attachment B-Building Coordinator and Floor Warden Responsibilities

First and foremost, as a volunteer, you should not place yourself in danger.

Building Evacuation:

Some reasons a building may need to be evacuated: fire, chemical spill, toxic or

explosive gases, violent behavior, a bomb threat.

Special considerations for evacuation:

Be familiar with special hazards in your area

Be familiar with equipment to assist persons with disabilities, such as EvacuTrac

Fire alarm pull stations:

Located near most building exit doors

Activate by pulling small tab

Fire alarm systems:

All fire alarm systems designed to notify persons to evacuate

Most have tone, visual, and voice messaging for evacuation instructions, others are

alarm only.

Department Emergency Plan:

Review your Dept. Emergency Plan

Floor Warden:

Help ensure safe building evacuation	 and communication of emergency information

persons evacuating the building.

Keep track of information about injured persons, known missing persons, persons

remaining in building.

Building Coordinator:

Collect information from Floor Wardens outside the building

Building Evacuation-Floor Wardens:

During an emergency: Put orange vest on

Evacuate occupants in their area

Direct occupants to exits

Make sure hazardous equipment is shut off

Close doors

Make sure no one is left behind

If someone refuses to leave, make note of their location and

provide that information to the Building Coordinator

Do not put yourself in harm’s way, if you feel you need to

evacuate without evacuating others, you may do so

If someone has trouble evacuating, help them to an

evacuation assistance location or area of refuge, usually

located in an enclosed stairwell

Once outside, report to the Building Coordinator with any info.

Assist Building Coordinator as needed.

Keep people away from the building

When police, fire or Building Coordinator give the all clear,

tell all persons all around the building they may re-enter

Emergency responders may silence the fire alarm while

investigating, this is not the all-clear signal. Keep

persons from entering the building until the all-clear is

received

Building Evacuation-Building Coordinators:

During an emergency:      Put on red vest

Grab notepad, pen, Building Plan

Exit the building

Go outside to the Building or Department Assembly Point

Take information from Floor Wardens on injured persons,

known missing persons, and persons remaining in bldg.

Seek out and provide information to first responders

If a stairway is full of smoke, go to another. If there is smoke in the hall, stay low,

cover you mouth with a damp cloth, stay close to and use the wall as a guide to

stairwell.

Major Disaster Assembly Areas:

Assist persons to get to these areas:

Old Main Lawn

South Campus Oval

Tennis Courts

Basic first aid and directions will be provided in these areas during major disasters.

Persons in blue vests will come to pick up Major Disaster Status forms from Bldg.

Coordinators and take them to the Emergency Operations Center.